Team 8
Methodology:

Robot Control	Node: ControlSubscribed topics: None / Published topics: /robot/robotnik_base_contol/cmd_vel / Parameters: / MAX_LIN_VEL / MAX_LIN_VEL / LIN_VEL_STEP_SIZE / ANG_VEL_STEP_SIZE / Methodology: / function getKey() → key / using tty stdin to read the input as a list of all keys have been pressed process the fist key. / Main() → publish / call the getkey at beginning. based on the key returned, do a check to increase linear or angular velocities but within the range. / If no key pressed for short time which we simulate with status / if status reached 10 then both linear and angular velocities decayes to 0.
Sensor Incorporating and Alignment	External Package / This package used for combine the bose laser data in one topic only. / Node: ira_laser_tools / Subscribed topics: / /robot/front_laser/scan / /robot/rear_laser/scan / Published topics: /scan_multi , /merged_cloud / Parameters: / destination_frame / angle_min / angle_min / angle_max / angle_increment / scan_time / range_min / range_max / Then use message_filters library in python to combine the odom and laser scan data and then publish to one topic.
Mapping with known poses	Node: mapping / Subscribed topics: /scan_multi / Published topics: /Map_known_Pose / Parameters: / sensor_model_p_occ value="0.75 / sensor_model_p_free" value="0.45" / sensor_model_p_prior" value="0.5" / robot_frame" value="robot_base_link" / map_frame" value="robot_map" / map_center_x" value="-50.0" / map_center_y" value="-50.0" / map_size_x" value="100.0" / map_size_y" value="100.0" / map_resolution" value="0.08" / map_publish_freq" value="2" / update_movement" value="0.03" / Methodology: Occupancy grid mapping with some modifications / The above are the parameters that algorithm needs to work. / 1- we get the robot position from the ground truth we have in the simulation which is the location of the robot base frame “robot_base_link” and the fixed frame in the environment “robot_map” by publishing tf transfom between the two frames we get the robot true position and orientation. / 2- every callback from the laser topic, get the true robot position and orientation then scan all the laser data which in the form of ( angle,distance) / - update the angle with the information you know about the robot orientation. / - Get the x , y associated with each laser beam (object location in meters) / - convert object location to indices, call bresenham to construct line from robot cell to object cell. / - for each point in the returned line pixels : / cell += inverse(free_probability) – inverse(prior_probability) / - except for the last cell (hit cell) / cell += inverse(occ_probability) – inverse(prior_probability) / 3- after processing all laser data: / retrieve P for all cells values and multiply by 100 and store in list int8 which is the type of the occupancy grid / 4- publich the map. / For bresenham algorithm we used it from geeksforgeeks.